## Slide 1
DIGITAL DESIGN & COMPUTER ARCHITECTURE
SMART WATER TANK
OVERFLOW PROTECTION
AND PUMP CONTROL SYSTEM
Design • Logic • Simulation in Logisim
LOW
FULL
AUTO PUMP CONTROL
TEAM MEMBERS
2620090006 | Sai Harsha
2620090013 | Kanduri Vishnu Preetham
2620090016 | Thumu Vilas
2620090023 | T. V. H. S. S. Jayasurya
SECTION: 9
FINAL PROJECT DEMONSTRATION

## Slide 2
DDCA PROJECT / 02
Introduction & Objective
A digital-logic approach to safer, smarter water storage
THE PROBLEM
Water tanks can overflow when a pump is left running. Manual monitoring also wastes time and may lead to water and electricity loss.
OUR IDEA
Use level sensors as digital inputs and logic circuitry to control a pump indicator automatically.
OBJECTIVES
•
Detect low-water and full-tank conditions
•
Turn the pump control output on/off logically
•
Verify the design using a Logisim simulation
HOW IT WORKS
LOW
FULL
SENSORS
PUMP
Sensor inputs → logic decision → pump output

## Slide 3
DDCA PROJECT / 03
Theory & Logic Circuit
Digital inputs represent water-level conditions
INPUTS & OUTPUT
L — Low-level condition 1 = water is low H — High-level / full sensor 1 = tank is full P — Pump command 1 = pump ON 0 = pump OFF
Design note: a real pump controller needs memory (latch/flip-flop) to keep the pump running between the low and full thresholds.
CONTROL LOGIC — CONCEPTUAL
LOW SENSOR L
FULL SENSOR H
CONTROL LATCH
PUMP OUTPUT
Set condition: low level detected • Reset condition: full tank detected
A latch provides the memory needed for automatic refill control; the exact Logisim implementation should match the circuit built by your team.

## Slide 4
DDCA PROJECT / 04
Circuit Design in Logisim
Gate-level control using two cross-coupled NOR gates (SR latch)
In Logisim: place 2 NOR gates, 2 input pins (LOW and FULL), connect feedback wires, and attach an LED to Q.

## Slide 5
DDCA PROJECT / 05
Simulation Results
Expected behavior for a latch-based refill controller
INPUT / EVENT
LOW SENSOR (L)
FULL SENSOR (H)
PUMP (P)
EXPECTED ACTION
Water below low mark
1
0
1
Pump starts
Water rising between sensors
0
0
1*
Pump keeps running
Tank reaches full mark
0
1
0
Pump stops
Normal level / no new event
0
0
0*
Pump remains off
*The output depends on the stored latch state when both sensors are 0. The memory element is what makes the system automatic.
Pump OFF / full reached
Pump ON / filling
Low-level trigger
This table describes the latch's stored-state behavior; the pump output between sensor thresholds depends on the previous state.

## Slide 6
DDCA PROJECT / 06
Conclusion & Applications
From a logic design to a practical water-saving idea
OUTCOME
•
Automatic pump start/stop logic
•
Reduces overflow risk
•
Demonstrates digital control
APPLICATIONS
•
Homes and apartments
•
Overhead and storage tanks
•
Schools, offices, small buildings
FUTURE IMPROVEMENTS
•
Add buzzer / overflow alarm
•
Add dry-run protection
•
Use relay driver and real sensors
KEY TAKEAWAY
Digital logic can make water management more reliable, efficient, and easier to monitor.
THANK YOU